## Slide 1
Smart Vending Machine Prototype
An Embedded System Based Automated Product Dispensing System
Vending System Flow
Arduino Control
Processes selection and logic
Servo Dispensing
Mechanism releases selected item
Keypad Input
User selects product code
Theme
Embedded Systems
Team member:
1.AB Siddik(EEE)
2.Arifa(CSE)
3.Al Amin(CSE)
4.Santa(EEE)

## Slide 2
Introduction & Problem Statement
What is a Smart Vending Machine?
An automated system that provides a product after a user makes a selection — no human operator required. Our prototype integrates embedded hardware components to achieve fully automated dispensing with real-time feedback and safety detection.
Core Hardware Components
Arduino microcontroller — main system controller
2×3 keypad — product selection input
16×2 I2C LCD display — system status output
Six 360° continuous-rotation servo motors
Mechanical dispensing mechanism
IR/obstacle sensor — product detection
Power supply — electrical distribution
Problem Statement
A functional vending machine prototype must address five core engineering challenges simultaneously:
Simple Selection
Product selection must be simple and intuitive for any user without prior training.
Automatic Dispensing
The selected product must dispense automatically upon keypad confirmation.
Delivery Confirmation
System must confirm the product reaches the collection area via sensor.
Failure Detection
Dispensing failure must be detected safely and reported to the user.
Motor Safety
Motor must not run indefinitely — a 10-second timeout enforces safe shutdown.

## Slide 3
Project Objectives
Six clearly defined engineering objectives guide the design, implementation, and testing of the Smart Vending Machine prototype from hardware assembly through software integration.
1
Functional Prototype
Build a functional vending machine with 6 product slots, each independently controlled by a dedicated servo motor and dispensing mechanism.
2
Keypad Interface
Select products using a 2×3 keypad interface (keys 1–6), providing a simple and intuitive user input method without additional hardware.
3
Servo Control
Control six 360° continuous-rotation servo motors independently via PWM signals on dedicated Arduino digital pins.
4
LCD Feedback
Display real-time system status using a 16×2 I2C LCD (address 0x27), including selection confirmation, dispensing status, and error messages.
5
Sonar Sensor Detection
Detect successful product delivery using an Sonar sensor positioned at the collection area to confirm product arrival.
6
10-Second Timeout
Implement a 10-second timeout to detect dispensing failure, stop the servo automatically, and prevent indefinite motor operation.

## Slide 4
Hardware Components & Pin Configuration
System Components Overview
Arduino Microcontroller
Main system controller — executes all logic, reads keypad input, drives servo PWM signals, and communicates with LCD and sensor.
2×3 Matrix Keypad
Product selection input device. Two rows and three columns provide keys 1–6, each mapped to a unique servo motor.
16×2 I2C LCD (0x27)
Displays system status messages including selection confirmation, dispensing progress, success, and failure notifications.
Six 360° Continuous-Rotation Servos
Each servo independently drives one product slot's mechanical dispensing mechanism via PWM on a dedicated digital pin.
Sonar Sensor
Positioned at the product collection area. Detects product arrival to trigger servo stop and success confirmation.
Arduino Pin Assignment Table
Component
Arduino Pin
Type
Keypad Row 1
D13
Digital I/O
Keypad Row 2
D12
Digital I/O
Keypad Column 1
D2
Digital I/O
Keypad Column 2
D8
Digital I/O
Keypad Column 3
D7
Digital I/O
Servo 1
D3
PWM Output
Servo 2
D5
PWM Output
Servo 3
D6
PWM Output
Servo 4
D9
PWM Output
Servo 5
D10
PWM Output
Servo 6
D11
PWM Output
LCD SDA
A4
I2C Data
LCD SCL
A5
I2C Clock
All servo pins (D3, D5, D6, D9, D10, D11) are hardware PWM-capable pins on the Arduino, required for precise servo signal generation.

## Slide 5
System Architecture
Control Flow — End to End
01
User Input
User presses a key (1–6) on the 2×3 keypad to select a product slot.
02
Arduino Processing
The Arduino microcontroller reads the keypad input, maps the key to the corresponding servo and pin number.
03
Servo Activation
The selected 360° servo is activated via PWM signal, driving the mechanical dispensing mechanism.
04
Product Dispensing
The mechanical dispensing mechanism moves the product toward the collection area.
05
Sensor Detection
The IR/obstacle sensor at the collection area detects product arrival and signals the Arduino.
06
LCD Confirmation
The 16×2 I2C LCD displays the final status — success or failure — to the user.
Product Selection Mapping (Key → Servo → Pin)
Keypad Key
Servo
Arduino Pin
Key 1
Servo 1
D3
Key 2
Servo 2
D5
Key 3
Servo 3
D6
Key 4
Servo 4
D9
Key 5
Servo 5
D10
Key 6
Servo 6
D11
Each keypad key maps directly and exclusively to one servo motor on a dedicated PWM pin. Only the selected servo activates — all other five servos remain stationary during any dispensing cycle.
6 Slots
Product slots
6 Servos
360° motors
1 Sensor
IR detection
1 LCD
I2C display

## Slide 6
Current Prototype: Hardware Control Stage
Current Stage: Keypad input + LCD feedback + six-servo control. Sonar sensor integration and 10-second timeout will be added in the next development phase.
Current Control Process — 8-Step Sequence
1
Keypad Input
User presses a key (1–6) on the 2×3 keypad to select a product slot.
2
Arduino Reads Selection
Arduino reads and identifies the selected product, mapping the key to the corresponding servo.
3
Servo Activation
The corresponding servo (1–6) is activated on its designated PWM pin.
4
Rotation Command
Servo rotates using

## Slide 7
360° Servo Motor Dispensing Mechanism
Continuous-Rotation Servo Based Dispensing
Unlike standard 180° positional servos, 360° continuous-rotation servo motors spin indefinitely in either direction when commanded — making them ideal for driving mechanical dispensing mechanisms that require sustained rotational motion to push or move a product.
Independent Channel Control
Each of the 6 product slots is assigned to one dedicated 360° continuous-rotation servo motor on its own PWM pin. Only the selected servo activates per dispensing cycle.
Mechanical Coupling
The selected servo continuously rotates the mechanical dispensing mechanism, which moves or pushes the selected product toward the collection area below.
PWM Signal Control
Arduino controls each servo via a PWM signal. The write value determines direction and speed: 120 = forward, 90 = stop, 60 = reverse.
Timed vs. Sensor Stop
Current prototype: servo runs for 8 seconds (timed). Final system: servo stops on IR sensor detection or 10-second timeout, whichever occurs first.
Servo Command Specifications
Command
Value
Behavior
servo.write(120)
120
Continuous forward rotation — dispensing active
servo.write(90)
90
Stop — neutral dead-band, no rotation
servo.write(60)
60
Continuous reverse rotation — retract if needed
Mechanical Motion Path
IR Sensor
Collection Area
Dispensing Mechanism
Product Slot
The 360° servo drives the mechanism continuously until the product clears the slot and reaches the collection area, where the IR sensor confirms arrival and triggers the stop command.

## Slide 8
Sensor-Based Product Detection & Safety
MAXIMUM SENSOR DETECTION TIMEOUT: 10 SECONDS — If the IR sensor does not detect the product within 10 seconds of servo activation, the Arduino automatically stops the servo to prevent motor damage and system lockup.
Success Path — Normal Dispensing Cycle
The IR/obstacle sensor is positioned at the product collection area to confirm successful dispensing. When a product is detected, the system immediately stops the servo and confirms success.
1
Servo Starts
Selected servo begins dispensing — servo.write(120) activates continuous rotation.
2
Product Moves
Product travels through the mechanical mechanism toward the collection area.
3
IR Detects Arrival
IR sensor at the collection area detects the product's physical presence.
4
Servo Stops
Arduino immediately issues servo.write(90) — servo halts at neutral.
5
LCD Confirms
LCD displays: "Product Dispensed Successfully"
6
System Ready
System resets and is ready for the next product selection.
Failure Detection — 10-Second Timeout Path
If the product is NOT detected within the 10-second window, the system enters the failure detection path to protect the motor and notify the user.
1
Timeout Elapses
10 seconds pass with no IR sensor detection — product did not reach collection area.
2
Auto Stop
Arduino automatically stops the servo — servo.write(90) — preventing indefinite operation.
3
Motor Protected
Prevents indefinite motor operation, overheating, and mechanical damage to the dispensing system.
4
LCD Failure Alert
LCD displays: "Dispensing Failed" — user is notified of the error condition.
5
Event Logged
System logs the failure event via Serial Monitor for debugging and maintenance records.
6
System Ready
System resets for next selection or operator troubleshooting intervention.

## Slide 9
System Control Flowchart
Complete System Logic Flow — From User Input to Final State
Sonar Detection
Was product detected?
Activate Dispense
Start 360° servo
Check Availability
Is product available?
User Selects
Choose product 1–6
2 States
Success (sensor detected) or Failure (timeout elapsed)

## Slide 10
Advantages, Limitations & Future Improvements
✅ Advantages
Fully automated product dispensing — no operator required
Simple and intuitive 2×3 keypad interface
Six independent 360° servo control channels
Real-time 16×2 LCD status feedback
IR sensor-based product delivery confirmation
10-second safety timeout prevents motor damage
Low-cost prototype design using standard components
Modular architecture allows easy expansion
⚠️ Limitations
Limited to 6 product slots in current design
Software still in prototype and testing stage
No payment system implemented in current version
Mechanical mechanism requires further optimization
Sensor accuracy depends on product positioning
Servo timing may require calibration per product type
🔜 Future Improvements
RFID / NFC / QR code payment integration
Mobile app or Bluetooth wireless control
Automatic stock monitoring system
IoT / cloud connectivity for remote management
Touchscreen interface upgrade
Expandable to 12+ product slots
Multiple redundant sensors for reliability
Advanced mechanical dispensing optimization

## Slide 11
Conclusion
Project Summary
This project demonstrates the integration of an Arduino microcontroller, 2×3 keypad, six 360° continuous-rotation servo motors, 16×2 I2C LCD display (address 0x27), IR/obstacle sensor, and mechanical dispensing mechanism to develop a fully automated vending machine prototype.
The current prototype successfully demonstrates keypad-based servo selection and LCD feedback — validating the core hardware control layer of the system. The next development stage adds IR sensor-based product confirmation and a 10-second timeout to detect dispensing failures and prevent indefinite motor operation, completing the closed-loop control system.
Key Technical Achievements
6 Servos
360° continuous-rotation, independently controlled
D3–D11
PWM pins for precise servo signal generation
0x27
I2C LCD address on A4/A5
10 sec
Safety timeout for dispensing failure detection
System Specifications at a Glance
Microcontroller
Arduino
Product Slots
6
Servo Type
360° Continuous
Servo Pins
D3,D5,D6,D9,D10,D11
Keypad Pins
D13,D12,D2,D8,D7
LCD Address
0x27 (A4/A5)
Rotate Command
servo.write(120)
Stop Command
servo.write(90)
Current Run Time
8 seconds
Sensor Timeout
10 seconds
THANK YOU